## Slide 1: AUTObREW: Automated all grain homebrewing system
Nick Anderson

## Slide 2: Brewing Process
All Grain Brewing
  Requires 4 vessels
    Hot Liquor Tank
      Used to heat water
    Mash Tun
      Used to convert water and grains, into liquid with fermentable sugars
    Brew Pot
      Used to sanitize the liquid fermentable sugars (remove bacteria) and apply hops and any other additional ingredients
    Fermenter
      Used to convert the fermentable sugars into alcohol and allow solids still in wort to settle down for filtering
  Traditional process requires siphoning between hot liquor tank/mash tun, and brew pot/fermenter
  Mash tun/Brew pot transition done by gravity feed
    Mash tun must be elevated above brew pot

## Slide 3: Brewing Process
Entire process can take >4 hours
  Most of the time spent hands on
    Siphoning, lifting, checking temperatures, monitoring fluid levels
Automation of process would reduce hands on time
  Hands on required for
    Adding/removing grains
    Removing liquid from fermenter
    Swapping hoses for mashing/sparging
    Monitoring fluid process/reaction

## Slide 4: Automated Process Overview
Requires a microcontroller to handle monitoring of levels and temperatures, and controlling pumps and valves.
  Dependent on state machine
Microcontroller would talk via network communications to a GUI
  GUI would be a programmed developed on PC to allow the user to set up temperatures and time durations prior to brew start.

## Slide 5: Automated Brew Setup - Hardware

## Slide 6: Automated Brew Setup – Inputs
Inputs
  Level Float Switches
    Contact Closure (digital hi/lo input)
    HLT
    Brew Pot
  Temperature Probes
    Thermocouple
    HLT
    Mash Tun
    Brew Pot
    Fermenter
  Flow Meter
    Determines when all liquid has been drained from vessel
    Hall Effect Pulse
    HLT
    Brew Pot

## Slide 7: Automated Brew Setup – Outputs
Outputs
  Solenoid Activates
    Controls plumbing routes
  Power Relay
    Controls Heating Elements
    Controls Pump Activation
    Cooling Element Activation

## Slide 8: Brew Process – Step 1
Filling Hot Liquor Tank
  Activate K1 to allow water source to fill HLT until level switch is activated.

## Slide 9: Brew Process – Step 2
Heat HLT to temperature setpoint
  Activate Power Relay to turn on heating element until temperature reaches setpoint

## Slide 10: Brew Process – Step 3
Transfer water from HLT to Mash Tun
  Activate K2 to allow flow from HLT to Mash Tun until no flow is seen on flow meter.

## Slide 11: Brew Process – Step 4
Keep temperature in Mash Tun at consistent temperature, either through letting liquid sit in Mash Tun, or filling HLT with water, heating, and running Mash Tun liquid through coils in HLT to transfer heat from HLT to Mash Tun liquid.

## Slide 12: Brew Process – Step 5
Transfer fluid from Mash Tun into Brew pot, while adding water from HLT to Mash Tun to make sure liquid in Brew Pot reaches desired fluid level.

## Slide 13: Brew Process – Step 6
Heat up Liquid in Brew Pot to a rolling boil.

## Slide 14: Brew Process – Step 7
Cool liquid in Brew Pot by putting cold water through wort chiller in brew pot. Exhaust from Wort Chiller (will be warm/hot from heat transfer) would go into HLT and exit out of overflow valve. When level in HLT reaches level switch, heating element will turn on to heat water for cleaning. Also pump liquid out of brew pot, and back into brew pot to aid in circulation of liquid, and heat loss.

## Slide 15: Brew Process – Step 8
Transfer cooled liquid into fermenter until flow meter indicates there is no more liquid in brew pot.

## Slide 16: Brew Process – Step 9
Control temperature of fermenter by measuring temperature, and controlling power relay to cooling device

## Slide 17: GUI
Will allow user to set up temperatures and time durations prior to starting process, and monitor state, temperature and time during.

## Slide 18: Issues
Plumbing
  Solenoid valves with desired configuration
  Ensuring all components are food grade
Electrical
  Examine power draw for all components
    Continuous and Inrush
    Determine order that components should be turned on
    Determines if single 120VAC or 240VAC source is required.
  Select microcontroller with adequate I/O to control devices with spare for unseen issues
Mechanical
  Create a frame to mount vessels and parts to allow for gravity fed legs where required.